## Slide 1
Chapter 5. Fourier Transform

## Slide 2
Metropolis algorithm for Monte Carlo
Simplex method for linear programming
Krylov subspace iteration (CG)
Decomposition approach to matrix computation (LU, Singular value)
The Fortran compiler
QR algorithm for eigenvalues
Quick sort
Fast Fourier transform
Integer relation detection
Fast multipole

## Slide 3: Fourier Transform
Fourier analysis and orthogonal functions
Discrete Fourier transform
Fast Fourier transform

## Slide 4: Periodic motion
Fourier first pointed out that an arbitrary periodic function f(t), with a period T, can be decomposed into a summation of simple harmonic terms, which are periodic functions of frequencies that are multiples of the fundamental frequency 1/T of the function f(t).
1/T, 2/T, 3/T, 4/T, ......

## Slide 5: Jean Baptiste Joseph Fourier
(21 March 1768 –
16 May 1830)
He was a French mathematician and physicist born in Auxerre and best known for initiating the investigation of Fourier series and their applications to problems of heat transfer and vibrations.
The Fourier transform and Fourier's Law are also named in his honor.
Fourier is also generally credited with the discovery of the greenhouse effect.

## Slide 6
Assuming that we have a time-dependent function f(t) with a period T, that is, f(t+T) = f(t), the Fourier theorem can be cast as a summation
which is commonly known as the Fourier series. Here w= 2p/T is the fundamental angular frequency and gj's are the Fourier coefficients, which are given by

## Slide 7
The Fourier theorem can be derived from the properties of the exponential functions
which form an orthonormal basis set in the region of one period of f(t):
where t0 is an arbitrary starting point, f*j (t) is the complex conjugate of fj (t), and djk is the Kronecker function. We can always take t0 = 0 for convenience, because it is arbitrary.

## Slide 8: Fourier series example: sawtooth wave
…
…
1
1
-1

## Slide 9: Sawtooth wave summation
Harmonics
Harmonic sums
1
2
3
n

## Slide 10: Sawtooth wave summation (continued)
Harmonics
Harmonic sums
5
10
50
n

## Slide 11: Fourier analysis and orthogonal functions
We can generalize the Fourier theorem to a nonperiodic function defined in a region of x∈[a, b] if we have a complete basis set of orthonormal functions fk(x) with

## Slide 12
For any arbitrary function f(x) defined in the region of x∈[a, b], it can be written as:
if the function is square integrable, defined by
the coefficients gj are given by

## Slide 13
The continuous Fourier transform is obtained if we restrict the series to the region of t ∈ [-T/2, T/2] and then extend the period T to infinity. Then the sum becomes an integral:
which is commonly known as the Fourier integral. The Fourier coefficient function is given by
The Fourier transform & the inverse Fourier transform

## Slide 14
Another convention for Fourier transform

## Slide 15
Fourier Transforms are used in
X-ray diffraction
Electron microscopy (and diffraction)
NMR spectroscopy
IR spectroscopy
Fluorescence spectroscopy
Image processing
Plane wave DFT calculations
etc.

## Slide 16: Application of Fourier transform: find out periodic signal in a noisy background
0.333 Hz

## Slide 17: Fourier Transform Magnitude and Phase
As with any complex quantity, we can decompose f(t) and F(w) into their magnitude and phase.
f(t) can be written: f(t) = Mag{f(t)} exp[ -i Phase{f(t)}]
where Mag{f(t)}2 is often called the intensity, I(t), and Phase{f(t)} is called the phase, f(t).
Analogously, F(w) = Mag{F(w)} exp[ -i Phase{F(w)}]
The Mag{F(w)}2 is called the spectrum, S(w), and the Phase{F(w)} is called the spectral phase, j(w).
Just as both the intensity and phase are required to specify f(t), both the spectrum and spectral phase are required to specify F(w), and hence f(t).

## Slide 18
w
d(w)
Fourier Transform of d(t) is 1/.
And the Fourier Transform of 1:
t
d(t)
w
1/
t
1

## Slide 19
Time Reversal
Pf)
is neglected for simplicity

## Slide 20
Fourier Transform for Real Functions
If f(t) is a real function, and F() = FR() + iFI()
F() = F*()

## Slide 21
Fourier Transform for Real Functions
If f(t) is a real function, and F() = FR() + iFI()
F() = F*()
FR() is even, and FI() is odd.
FR() = FR()
FI() = FI()
Magnitude spectrum |F()| is even, and phase spectrum () is odd.

## Slide 22
Fourier Transform for Real Functions
If f(t) is real and even
F() is real
If f(t) is real and odd
F() is pure imaginary
Pf)
Pf)
Even
Real
Odd
Real



## Slide 23
Intensity and Phase of a Gaussian
The Gaussian is real, so its phase is zero.
Time domain:
Frequency domain:
So the spectral phase is zero, too.
A Gaussian transforms
to a Gaussian

## Slide 24
Scale Theorem
The Fourier transform of a scaled function, f(at):
If a < 0, the limits flip when we change variables, introducing a minus sign, hence the absolute value.
Assuming a > 0, change variables: u = at
Proof:

## Slide 25
The Scale Theorem in action
f(t)
F(w)
t
t
w
w
t
w
Short pulse
Medium- length pulse
Long pulse
The shorter the pulse, the broader the spectrum!
This is the essence of the Uncertainty Principle!

## Slide 26
The Fourier Transform of a sum of two functions
Also, constants factor out.
f(t)
g(t)
t
t
t
w
w
w
F(w)
G(w)
f(t)+g(t)
F(w) + G(w)

## Slide 27
Shift Theorem

## Slide 28
Fourier Transform of the complex conjugate of a function
Proof:

## Slide 29
Derivative Theorem
The Fourier transform of a derivative of a function, f’(t):
Proof:

## Slide 30: Modulation Theorem Fourier Transform of E(t) cos(w0 t)

## Slide 31: Fourier Transform of a convolution
The convolution of two functions f1(t) and f2(t) is defined as:

## Slide 32: Properties of Convolution

## Slide 33
Time Domain
Frequency Domain
convolution
multiplication

## Slide 34
Parseval’s Theorem
Energy in temporal space is the same as the energy in spectral space!

## Slide 35: The 2D Fourier Transform
F (2){f(x,y)} = F(kx,ky)
= f(x,y) exp[-i(kxx+kyy)] dx dy
If f(x,y) = fx(x) fy(y),
then the 2D FT splits into two 1D FT's.
But this doesn’t always happen.
F (2){f(x,y)}
x
y
f(x,y)

## Slide 36: Fourier Transform Magnitude and Phase
Pictures reconstructed
using the spectral phase
of the other picture
The phase of the Fourier transform (spectral phase) is much more important than the magnitude in reconstructing an image.
Rick
Linda
Mag{F [Linda]}
Phase{F [Rick]}
Mag{F [Rick]}
Phase{F {Linda]}

## Slide 37
Three dimensions
The space defined by q is usually called the momentum space.

## Slide 38: Discrete Fourier transform
f(x): a physical quantity obtained from measurements. The measurements are between x=0 and x=L.
The data are measured at evenly spaced points with each interval h=L/N, where N is the total number of data points.
Assume that the data repeat periodically outside the region of x∈[0,L], which is equivalent to the periodic boundary condition on the finite system.
The corresponding wavenumber in the momentum space is then discrete too, with an interval k=2p/L.

## Slide 39
Assume that the data repeat periodically outside the region of x∈[0,L], which is equivalent to the periodic boundary condition on the finite system.
0
1
2
3
N-1
N
…
Derivation of Discrete Fourier transform

## Slide 40
(1) Assume periodicity
Use trapezoidal Rule
(2) Numerical integration

## Slide 41
The exponential functions in the series form a discrete basis set of orthogonal functions:
Discrete Fourier transform (DFT)
Periodicity:

## Slide 42
DFT vs. Fourier transform
t=kL/N
Time range: between 0 and L

## Slide 43: Code example
f1(x)=sin(2px)+sin(50px+1)+sin(104px+2)
f2(x)=-sin(2px)+sin(50px+2)+sin(104px+1)
x within [0,1].

## Slide 44
Fourier.cpp
0 -1.27637e-14 0 1.27637e-14
1 -1.8072e-14 -90.5097 90.5097
2 -1.26645e-14 -4.54899e-15 1.34568e-14
…
24 -8.24868e-14 4.43416e-14 9.36496e-14
25 76.1613 -48.9026 90.5097
26 6.77505e-14 -4.97099e-14 8.4031e-14
…
51 -1.74382e-13 -7.42175e-14 1.89519e-13
52 82.3002 37.6653 90.5097

## Slide 45
Aliasing
Intensity [a.u.]
2
3
4
5
6
There are many sine-waves, SAMPLED with the same measurements. Which is the correct one?

## Slide 46
For a given sampling interval, the maximum recordable frequency of 1/(2a) is known as the Nyquist frequency
Nyquist frequency = (1 / 2) * N / L when N / L is the sampling frequency.
If f(x) contains frequencies greater than the Nyquist frequency 1/(2a), then it is said to be undersampled
Nyquist frequency
a = L / N

## Slide 47: Fast Fourier transform
The straightforward discrete Fourier transform algorithm is very inefficient, because the computing time needed is proportional to N2.
Speed: FFT (fast Fourier transform).
Basic idea: N number DFT-> two N/2 DFT
by Cooley and Tukey (1965)
FFT
Discrete FT

## Slide 48: 4-Point DFT case
when N=4:
Decimate in time into 2 series:
n = {0 , 2} and {1, 3}
Here the factor 1/sqrt(N) have been ignored.

## Slide 49: 4-Point FFT Flow Diagram
The 2 DFT’s:
for k=0,1,2,3
For k=0 only:
A ‘flow-diagram’ of it:
x(0)
x(2)
W40
+
x(1)
x(3)
W40
+
W40
+
This is for only 1/4 of the
whole diagram !

## Slide 50: A Complete Diagram
x(0)
x(1)
x(2)
x(3)
X4(0)
X4(1)
X4(2)
X4(3)
0
2
0
2
3
2
1
0
Note:

## Slide 51: Fast Fourier transform: general discussion
The simplest fast Fourier transform algorithm is accomplished with the observation that we can separate the odd and even terms in the discrete Fourier transform as

## Slide 52
This process can be repeated further and further until eventually we have only two terms in each summation if N = 2M, where M is an integer.
There is one more symmetry between gj for j < N/2 and gj for j ≥ N/2:
where w = e-i2p/N and j = 0, 1, . . . , N/2-1.
Proof:

## Slide 53
After the summation is decomposed M times, we need to add individual data points in pairs.
However, due to the sorting of the odd and even terms in every level of decomposition, the points in each pair at the first level of additions can be very far apart in the original data string.
For example, if N=8, the decomposition is like:
0-7
0 2 4 6 1 3 5 7
0:4 2:6 1:5 3:7

## Slide 54
Cooley and Tukey (1965) found that if we record the data string index with a binary number, a bit-reversed order will put each pair of data points next to each other for the summations at the first level.
000
001
010
011
100
101
110
111
0
1
2
3
4
5
6
7
000
100
010
110
001
101
011
111
0
4
2
6
1
5
3
7
bit-reversed order
0-7
0 2 4 6 1 3 5 7
0:4 2:6 1:5 3:7

## Slide 55
gj (0, 1, 2, 3, 4, 5, 6, 7)=xj (0, 2, 4, 6)+wj yj (1, 3, 5, 7)
wj=exp(-i2pj/8) (j=0-3)
g0=x0+w0y0 g1=x1+w1y1 g2=x2+w2y2 g3=x3+w3y3
g4=x0-w0y0 g5=x1-w1y1 g6=x2-w2y2 g7=x3-w3y3
1
wwj=exp(-i2pj/4) (j=0-1)
x0=xx0+ww0xy0 x1=xx1+ww1xy1 y0=yx0+ww0yy0 y1=yx1+ww1yy1
x2=xx0-ww0xy0 x3=xx1-ww1xy1 y2=yx0-ww0yy0 y3=yx1-ww1yy1
2
xj (0, 2, 4, 6) = xxj (0, 4) + wwj xyj (2, 6)
yj (1, 3, 5, 7) = yxj (1, 5) + wwj yyj (3, 7)
wwwj=exp(-i2pj/2) (j=0) www0=1
xx0=f0+f4 xy0=f2+f6 yx0=f1+f5 yy0=f3+f7
xx1=f0-f4 xy1=f2-f6 yx1=f1-f5 yy1=f3-f7
3
xxj(0,4)=xxxj(0)+wwwj xxyj(4) xyj(2,6)=xyxj(2)+wwwj xyyj(6)
yxj(1,5)=yxxj(1)+wwwj yxyj(5) yyj(3,7)=yyxj(3)+wwwj yyyj(7)

## Slide 56
f0 f4 f2 f6 f1 f5 f3 f7
From bottom to top
xx1
xy0
xy1
yx0
yx1
yy0
yy1
xx0
x1
x2
x3
y0
y1
y2
y3
x0
g1
g2
g3
g4
g5
g6
g7
g0

## Slide 57
翻花绳

## Slide 58: Code example
FFT.cpp
f1(x)=sin(2px)+sin(50px+1)+sin(104px+2)
within [0,1].
With the FFT algorithm, the computing time is reduced.
A careful analysis shows that the total computing time is proportional to N log2N instead of to N2.

## Slide 59: FFTW
The Fastest Fourier Transform in the West (FFTW) is a software library for computing discrete Fourier transforms developed by Matteo Frigo and Steven G. Johnson at the Massachusetts Institute of Technology.
Website: http://www.fftw.org
Stable version: 3.3.8
Any N is allowed
License: GPL, commercial

## Slide 60
See also
https://people.sc.fsu.edu/~jburkardt/f_src/fftw3/fftw3.html
FFTW example
fftw3_test.f90
ifort fftw3_test.f90 -I/opt/intel/mkl/include/fftw -mkl=sequential

## Slide 61
Homework
1. One-dimensional Kronig-Penney problem
Periodic potential
LW
LB
U0
U0= 2 eV, LW = 0.9 nm and LB = 0.1 nm (a = 1 nm).
a
Using FFT, find the lowest three eigenvalues of the eigenstates that satisfy

## Slide 62
FFT

## Slide 63
2. Detecting periodicity: Download the file called sunspots.txt, which contains the observed number of sunspots on the Sun for each month since January 1749.
Write a program to calculate the Fourier transform of the sunspot data and then make a graph of the magnitude squared |ck|2 of the Fourier coefficients as a function of k—also called the power spectrum of the sunspot signal. You should see that there is a noticeable peak in the power spectrum at a nonzero value of k. Find the approximate value of k to which the peak corresponds. What is the period of the sine wave with this value of k?